## Slide 1
Agenda
1
PDU Flow through the Layered Architecture
Interaction of Layers – Active Request/Passive Request
Interaction of Layers – Communication
Interaction of Layers - Memory
Interaction of Layers – Diagnostics

## Slide 2
Interaction of Layers - Communication
2

## Slide 3
Interaction of Layers - Communication
3
PDU Router
Provides routing of PDUs between different abstract communication controllers and upper Layers
Scale of the Router is ECU specific
Provides TP routing on-the-fly.
Transfer of TP data is started before full TP data is buffered.
COM
Provides routing of individual signals or groups of signals between different I-PDUs.
Communication Manager
Start and Shutdown the hardware units of the communication systems via the interfaces.
Control PDU groups

## Slide 4
Communication
4
The main elements to describe communication in the System Template are the Signals (System Signals and ISignals), PDUs (I-Pdus, N-Pdus and NmPdus) and Frames
A Frame is a piece of information that is exchanged over the communication channels. It has a payload section of a certain length in bytes, which contains an arbitrary number of non-overlapping PDUs
A PDU (Protocol Data Unit) is the information delivered through a network layer. For the network to understand which layer is being discussed, a single-letter prefix is added to the PDU
I-PDU - Interaction Layer Protocol Data Unit (assembled and disassembled in COM) In the case of external communication the Interaction Layer packs one or more signals into assigned I-Pdus and passes them to the underlying layer for transfer between nodes in a network
N-PDU - Network Layer Protocol Data Unit (assembled and disassembled in a Transport Protocol module).
L-PDU - Data Link Layer Protocol Data Unit (assembled and disassembled in AUTOSAR Hardware Abstraction layer).

## Slide 5
Communication
5
In case no multiplexing is performed the I-PDUs of COM that fit into one frame are passed directly via the PDU Router to the communication interfaces
For CAN and LIN the maximum L-PDU length is 8 bytes
For FlexRay the maximum L-PDU length is 254 bytes
Large I-PDUs that are too long to fit into one L-Pdu and I-PDUs which contain dynamic signals are routed via the Transport Layer to the communication interfaces
All I-PDUs from the DCM are transported via the Transport Protocol
If multiplexing is performed an IPdu is routed between the IPdu Multiplexer and the Interface Layer or Transport Layer

## Slide 6
Interaction of Layers – Active Request (R4.0.3)
6
RTE
SWC
ComM
CanSm
Nm
CanIf
CanNm
2.ComM_RequestComMode(FULL)
4.CanIf_SetControllerMode()
7.CanSM_ControllerModeIndication()
11.Nm_NetworkMode()
1.Rte_Call_<port>_ReqMode(FULL)
13.Rte_Ports_UserMode_P()[n].Switch_currentMode()
3.CanSm_RequestComMode(FULL)
9.Nm_NetworkRequest()
10.CanNm_NetworkRequest()
Can Driver
5.Can_SetControllerMode()
12.ComM_Nm_NetworkMode()
Repeat Msg State
Normal Operation
Ready Sleep State
Prepare Bus Sleep
N/W Rel
Count Expires
Rep Msg Timer expires
NM Frame Transmission is possible
8.ComM_BusSM_ModeIndication()
6.CanIf_ControllerModeIndication()
BswM indication from ComM & CanSM in not included to start the Ipdu-Group

## Slide 7
Interaction of Layers – Passive Request (e.g. Bus WUP) (R4.0.3)
7
RTE
ComM
CanSm
Nm
CanIf
CanNm
3.CanIf_SetControllerMode()
6.CanSM_ControllerModeIndication()
10.Nm_NetworkMode()
SWC
2.CanSm_RequestComMode(FULL)
8.Nm_PassiveStartUp()
9.CanNm_PassiveStartUp()
Can Driver
4.Can_SetControllerMode()
11.ComM_Nm_NetworkMode()
Repeat Msg State
Ready Sleep State
Prepare Bus Sleep
Count Expires
EcuM
1.ComM_EcuM_WakeUpIndication()
12. Rte_Ports_UserMode_P()[n].Switch_currentMode()
Rep Msg Timer expires
7.ComM_BusSM_ModeIndication()
5.CanIf_ControllerModeIndication()
NM Frame Transmission is possible
BswM indication from ComM & CanSM in not included to start the Ipdu-Group

## Slide 8
Interaction of Layers – Active Request (Network Release) (R4.0.3)
8
RTE
ComM
CanSm
Nm
CanIf
CanNm
8/16.CanIf_SetControllerMode()
11/19.CanSM_ControllerModeIndication()
5.Nm_PrepareBusSleepMode()
SWC
7.CanSm_RequestComMode(Silent)
3.Nm_NetworkRelease()
4.CanNm_NetworkRelease()
Can Driver
9/17.Can_SetControllerMode()
6.ComM_Nm_PrepareBusSleepMode()
Rte_Ports_UserMode_P()[n].Switch_currentMode()
12/20.ComM_BusSM_ModeIndication()
10/18.CanIf_ControllerModeIndication()
13.Nm_BusSleepMode()
14.ComM_Nm_BusSleepMode()
1.Rte_Call_<port>_ReqMode(NO)
2.ComM_RequestComMode(NO)
Repeat Msg State
Normal Operation
Ready Sleep State
Prepare Bus Sleep
N/W Rel
Count Expires
Rep Msg Timer expires
NO NM Frame Transmission is possible
15.CanSm_RequestComMode(NO)
BswM indication from ComM & CanSM in not included to start the Ipdu-Group

## Slide 9
Interaction of Layers – Communication (Transmit) (R4.0.3)
9
AUTOSAR COM
PDU Router
CAN
Interface
CAN
Driver
µC
CAN
3.PduR_ComTransmit()
4.CanIf_Transmit()
5.Can_Write()
6.Copy L-PDU into
CAN Hardware
7. Transmit Interrupt
8.CanIf_TxConfirmation()
10.Com_TxConfirmation()
9.PduR_CanIfTxConfirmation()
SWC
1.Rte_Write_Xxx()
RTE
2.Com_SendSignal()
11. Rte_COMCbkTAck_<sn>()

## Slide 10
Interaction of Layers – Communication (Receive) (R4.0.3)
10
AUTOSAR COM
PDU Router
CAN
Interface
CAN
Driver
µC
CAN
1.Receive Interrupt
2.CanIf_RxIndication()
4.Com_RxIndication()
3.PduR_CanIfRxIndication()
SWC
6.Rte_Read_Xxx()
RTE
7. Com_ReceiveSignal()
5. Rte_COMCbk_<sn>()

## Slide 11
Interaction of Layers – Diagnostics (Receive) (R4.0.3)
11
Diagnostic Communication Manager (DCM)
PDU Router
CAN Transport Layer
CAN
Interface
CAN
Driver
µC
CAN
Diagnostic Event Manager (DEM)
1.Receive Interrupt
2.CanIf_RxIndication()
3.CanTp_RxIndication()
7.Dcm_CopyRxData()
4.PduR_CanTpStartOfReception ()
5.Dcm_StartOfReception()
10.Dem_EnableDTCStorage()
(for UDS Service 0x85)
9.Dcm_TpRxIndication()
6.PduR_CanTpCopyRxData ()
8.PduR_CanTpRxIndication ()

## Slide 12
Interaction of Layers – Diagnostics (Transmit) (R4.0.3)
12
Diagnostic Communication Manager (DCM)
PDU Router
CAN Transport Layer
CAN
Interface
CAN
Driver
µC
CAN
Diagnostic Event Manager (DEM)
1.PduR_DcmTransmit()
2.CanTp_Transmit()
3.PduR_CanTpCoppyTxData()
4.Dcm_CopyTxData()
5.CanIf_Transmit()
6.Can_Write()
7.Copy L-PDU into
CAN Hardware
8.Transmit Interrupt
9.CanIf_TxConfirmation()
10.CanTp_TxConfirmation()
11.PduR_CanTpTxConfirmation()
12.Dcm_TpTxConfirmation()
Function Inhibition Manager (FIM)
FiM_DemTriggerOnEventStatus ()
BSW Module
Dem_ReportErrorStatus()

## Slide 13
Interaction of Layers - Memory
13
COM Drivers
Memory Hardware Abstraction
µC
Memory Drivers
SPI
EEPROM
Flash
External Flash Driver
Memory Abstraction Interface
External
EEPROM Driver
EEPROM Abstraction
Flash EEPROM Emulation
SPI Handler
Driver
EEPROM Driver
Internal Flash Driver

## Slide 14
Interaction of Layers - Memory Read (R4.0.3)
14
RTE
SWC
NVRAM Manager
Memory Abstraction Interface
EEPROM Abstraction(EA)
Flash EEPROM Emulation(FEE)
EEPROM Driver
Internal Flash Driver
NvM_ReadBlock()
MemIf_Read()
Ea_Read()
EeP_Read()
Fee_Read()
Fls_Read()
Ea_JobEndNotification()
NvM_JobEndNotification()
Fee_JobEndNotification()
SWC
Rte_Call_<port>_ReadBlock()
Rte_Call_Xxx()

## Slide 15
Interaction of Layers - Memory Write (R4.0.3)
15
RTE
SWC
NVRAM Manager
Memory Abstraction Interface
EEPROM Abstraction(EA)
Flash EEPROM Emulation(FEE)
EEPROM Driver
Internal Flash Driver
NvM_WriteBlock()
MemIf_Write()
Ea_Write()
EeP_Write()
Fee_Write()
Fls_Write()
NvM_JobEndNotification()
SWC
Rte_Call_<port>_ReadBlock()
Rte_Call_Xxx()
Ea_JobEndNotification()
Fee_JobEndNotification()
NvM_JobEndNotification()