## Slide 1
Agenda
AUTOSAR Introduction
AUTOSAR Vision
AUTOSAR Concept
AUTOSAR ECU Software Architecture
AUTOSAR Benefits
AUTOSAR Layered Software Architecture

## Slide 2: AUTOSAR Introduction
AUTOSAR (AUTmotive Open System ARchitecture) is a revolutionary milestone in the development of Automotive E/E Systems. The development partnership established by leading OEM’s and Suppliers had defined an open reference architecture for ECU software.
The idea behind AUTOSAR initiative is found in 2003 by Automotive OEM’s and Suppliers to avoid re-developing of similar software components.

## Slide 3: AUTOSAR Partners and Members
66 Associate Members
6 Attendees
9 Core Partners
12 Development Members
48 Premium Members
General OEM’s
Generics Tier1’s
General Software
Semicon’s
Tools & Services

## Slide 4: AUTOSAR Introduction Continued
  Provides a conceptual layered software architecture
  Provides mapping of the identified BSW modules to software layers
  Automotive ECUs having the following properties can adapt to AUTOSAR
    Strong interaction with hardware (sensors and actuators)
    Connection to vehicle network via CAN, LIN, FlexRay or Ethernet
    Microcontrollers from 16 to 32 bit
    Real Time Operating System
  Extensibility
    Modules can be added or the functionality of existing ones can be extended,
    but their configuration has to be considered in the Basic SW configuration
    process
    Complex drivers can easily be added

## Slide 5: AUTOSAR– Vision
AUTOSAR vision is an improved complexity management of highly Integrated E/E architectures through an increased Reuse and Exchangeability of SW Modules between OEMs and suppliers.
Platform A.1
OEM A
Platform A.n
Platform B.1
OEM B
Platform B.n
Platform C.1
OEM C
Platform C.n
Suppliers
Chassis
Safety
Telematics
Multimedia
Exchangeability between
Vehicle Platforms
Manufacture’s Applications
Exchangeability between
Suppliers Solutions

## Slide 6: AUTOSAR Concepts
Architecture
Interfaces
Specification of Interfaces of typical Automotive
Applications from all domains in terms of syntax and semantics
Methodology
Exchange formats or description templates to enable a
Seamless Configuration process of BSW stack
and the Integration of application software in ECU’s and it
includes even the methodology how to use this framework.
Software architecture including a complete Basic or
Environmental Software Stack for ECUs –AUTOSAR Basic Software

## Slide 7: AUTOSAR – ECU Software Architecture
AUTOSAR Interface
Standardized AUTOSAR Interface
Standardized Interface
AUTOSAR layer model offers…
Modular Components with defined interfaces
Hardware Independent Software layer
Transferability of modules
Decoupled Basic Software and Application Components using RTE
ECU-Hardware
AUTOSAR Runtime Environment (RTE)
Actuator
Software
Component
AUTOSAR Interface
Application
Software
Component
Sensor
Software
Component
Application
Software
Component
..............
AUTOSAR Software
Basic Software
Standardized Interface
AUTOSAR Interface
AUTOSAR Interface
AUTOSAR Interface
Microcontroller Abstraction
Standardized AUTOSAR Interface
Services
Standardized Interface
ECU
Abstraction
AUTOSAR Interface
Standardized Interface
Complex
Device
Drivers
AUTOSAR Interface
Standardized Interface
Communication
Standardized Interface
Standardized Interface
Operating
System
Standardized Inteface

## Slide 8: AUTOSAR – ECU Software Architecture Continuation
AUTOSAR Interface:
An "AUTOSAR Interface" defines the information exchanged between software components and/or BSW modules.
Standardized AUTOSAR Interface:
A "Standardized AUTOSAR Interface" is an "AUTOSAR Interface" whose syntax and semantics are standardized in AUTOSAR. The "Standardized AUTOSAR Interfaces" are typically used to define AUTOSAR Services, which are standardized services provided by the AUTOSAR Basic Software to the application Software-Components.
Standardized Interface:
“Standardized Interfaces" are typically used between software-modules which are always on the same ECU.

## Slide 9: Change in Automotive Development
Hardware- and software will be widely independent of each other.
Development processes will be simplified.
This reduces development time and costs.
Reuse of software increases at OEM as well as at suppliers.
This enhances also quality and efficiency.

## Slide 10: AUTOSAR Layered Software Architecture
The Layered Software Architecture describes the software architecture of AUTOSAR:
it describes in an top-down approach the hierarchical structure of AUTOSAR software and
maps the Basic Software Modules to software layers and
shows their relationship.
AUTOSAR extensibility
The AUTOSAR Software Architecture is a generic approach:
Standard modules can be extended in functionality, while still being compliant,
still, their configuration has to be considered in the automatic Basic SW configuration process!
non-standard modules can be integrated into AUTOSAR-based systems as Complex Drivers and
further layers cannot be added.

## Slide 11: Generic Layered Architecture
Application
Middleware
OS + Device Drivers
Hardware
Generic layered architecture allows two different systems to communicate despite of their core architecture (hardware or software)
Layered architecture provides standard methodology to design flexible, robust and interoperable architecture

## Slide 12: Overview of Software Layers : Top View
Application Layer
Basic Software (BSW)
Runtime Environment (RTE)
Microcontroller
The AUTOSAR Architecture distinguishes on the highest abstraction level between three software layers : Application, Runtime Environment and Basic Software which run on a Microcontroller.

## Slide 13: Overview of Software Layers : Coarse View
MICROCONTROLLER
MICROCONTROLLER ABSTRACTION LAYER
RUN TIME ENVIRONMENT
APPLICATION LAYER
SERVICES LAYER
ECU ABSTRACTION LAYER
COMPLEX DRIVERS

## Slide 14: Microcontroller Abstraction Layer
The Microcontroller Abstraction Layer is the lowest software layer of the Basic Software.
It contains internal drivers, which are software modules with direct access to the microcontroller and internal peripherals.
Task
Make higher software layers independent of microcontroller

## Slide 15: ECU Abstraction Layer
The ECU Abstraction Layer interfaces the drivers of the Microcontroller Abstraction Layer. It also contains drivers for external devices.
It offers an API for access to peripherals and devices regardless of their location (μC internal/external) and their connection to the μC (port pins, type of interface)
Task
Make higher software layers independent of ECU hardware layout

## Slide 16: Complex Drivers
The Complex Drivers Layer spans from the hardware to the RTE.
It offers an API for access to peripherals and devices regardless of their location (μC internal/external) and their connection to the μC (port pins, type of interface)
Task
Provide the possibility to integrate special purpose functionality, e.g. drivers for devices:
which are not specified within AUTOSAR,
with very high timing constrains or
for migration purposes etc.

## Slide 17: Services Layer
The Services Layer is the highest layer of the Basic Software which also applies for its relevance for the application software: while access to I/O signals is covered by the ECU Abstraction Layer, the Services Layer offers
Operating system functionality
Vehicle network communication and management services
Memory services (NVRAM management)
Diagnostic Services (including UDS communication, error memory and fault treatment)
ECU state management, mode management
Logical and temporal program flow monitoring (Wdg manager)
Task
Provide basic services for applications
and basic software modules.

## Slide 18: Runtime Environment (RTE)
The RTE is a layer providing communication services to the application software (AUTOSAR Software Components and/or AUTOSAR Sensor/Actuator components).
Above the RTE the software architecture style changes from “layered“ to “component style“.
The AUTOSAR Software Components communicate with other components (inter and/or intra ECU) and/or services via the RTE.
Task
Make AUTOSAR Software Components independent from the mapping to a specific ECU.

## Slide 19: Application Layer and RTE
RTE is a layer providing communication services to the application software
AUTOSAR Software Components communicate with other components (inter
and/or intra ECU) and/or services via the RTE
Application Layer
Actuator
Software
Component
Sensor
Software
Component
RTE
Basic Software
Interfaces to (e.g.)
I/O HW Abstraction (access to I/O signals)
Memory Services (access to calibration data)
System Services (access to Error Manager)

## Slide 20: Overview of Software Layers : Detailed View
Complex
Drivers
Microcontroller
AUTOSAR Runtime Environment (RTE)
Microcontroller Drivers
Memory Drivers
I/O Drivers
I/O Hardware Abstraction
Memory Hardware Abstraction
Memory Services
System Services
Onboard Device Abstraction
Communication Drivers
Communication Hardware Abstraction
Communication Services
Application Layer

## Slide 21: Overall Basic Software Architecture

## Slide 22: Communication Stack - CAN
AUTOSAR COM, PDU Router, IPDUM, Generic NM Interface and Diagnostic Communication Manager are the same for all vehicle network systems
A signal gateway is part of AUTOSAR COM to route signals
PDU (frame) based Gateway is part of PDU Router
IPDU multiplexing provides the possibility to add information to enable multiplexing of I-PDUs (different contents but same IDs)
Generic NM Interface contains only a dispatcher
CAN NM is specific for CAN networks & will be instantiated per CAN vehicle network system
CAN State Manager handles the Start and Stop communication on CAN bus

## Slide 23: Communication Stack – LIN
A LIN 2.1 compliant communication stack with
  Schedule table manager for transmitting LIN frames and to handle requests to switch to other schedule tables
  Transport protocol, used for diagnostics
  A Wakeup and Sleep Interface

## Slide 24: Communication Stack – FlexRay